## Slide 1: Basic Processing Unit

## Slide 2: Overview
Processor is also called Instruction Set Processor (ISP)
Central Processing Unit (CPU)
A typical computing task consists of a series of steps specified by a sequence of machine instructions that constitute a program.
An instruction is executed by carrying out a sequence of more rudimentary operations.

## Slide 3
Some Fundamental Concepts
Execution of a Complete Instruction
Hardwired Control
Microprogrammed Control

## Slide 4
Processor fetches one instruction at a time and perform the operation specified.
Instructions are fetched from successive memory locations until a branch or a jump instruction is encountered.
Processor keeps track of the address of the memory location containing the next instruction to be fetched using Program Counter (PC).
Instruction Register (IR)

## Slide 5
Three steps performed by the processor to execute an instruction
1) Fetch the contents of the memory location pointed to by the PC. The contents of this location are loaded into the IR (fetch phase).
IR ← [[PC]]
2) Assuming that the memory is byte addressable, increment the contents of the PC by 4 (fetch phase).
PC ← [PC] + 4
3) Carry out the actions specified by the instruction in the IR (execution phase).

## Slide 6
Registers,
ALU and interconnecting bus -Datapath

## Slide 7
Executing an instruction has one or more of the following operations in sequence
Transfer a word of data from one processor register to another or to the ALU.
Perform an arithmetic or a logic operation and store the result in a processor register.
Fetch the contents of a given memory location and load them into a processor register.
Store a word of data from a processor register into a given memory location.

## Slide 8: Register Transfers
B
A
Z
ALU
Y
in
Y
Z
in
Z
out
R
i
in
R
i
R
i
out
b
us
Internal processor
Constant 4
MUX
Figure 7.2. Input and output gating for the registers in Figure 7.1.
Select
Two control Signals
1)Place the content of register to bus,
Riout is set to 1
2)Load the data on bus to register ,
Riin is set to 1
Example
Transfer content of R1 to R4
R1out is set to 1
R4in is set to 1

## Slide 9
All operations and data transfer takes place within time period defined by processor clock
The control signals are asserted at the start of the clock cycle
Registers consists of edge-triggered flip-flops
In another scheme, data transfer may use both rising and falling edges of the clock
When edge-triggered flip-flops are not used, two or more clock signals may be needed for proper transfer of data, which is known as multiphase clocking

## Slide 10: Performing an Arithmetic or Logic Operation
The ALU is a combinational circuit that has no internal storage.
ALU gets the two operands from MUX and bus. The result is temporarily stored in register Z.
Example - Add the contents of register R1 to those of R2 and store the result in R3
  R1out, Yin
  R2out, Select Y, Add, Zin
  Zout, R3in

## Slide 11: Fetching a Word from Memory
Address into MAR; issue Read operation; data into MDR.
4 control signals
MDRin, MDRout – internal bus
MDRinE, MDRoutE – external bus

## Slide 12
The response time of each memory access varies (cache miss, memory-mapped I/O,…).
The processor waits until it receives an indication that the requested operation has been completed (Memory-Function-Completed, MFC).
Example - Move (R1), R2
MAR ← [R1]
Start a Read operation on the memory bus
Wait for the MFC response from the memory
Load MDR from the memory bus
R2 ← [MDR]
  R1out,MARin, Read
  MDRinE, WMFC
  MDRout, R2in

## Slide 13: Storing a word in memory
Address is loaded to MAR
Data is loaded into MDR and Write Command is issued
Example Move R2,(R1)
  R1out,MARin
  R2out,MDRin,Write
  MDRoutE,WMFC

## Slide 14
Some Fundamental Concepts
Execution of a Complete Instruction
Hardwired Control
Microprogrammed Control

## Slide 15: Execution of a Complete Instruction
Add (R3), R1
Fetch the instruction
Fetch the first operand (the contents of the memory location pointed to by R3)
Perform the addition
Load the result into R1

## Slide 16
Add (R3), R1

## Slide 17: Branch Instructions
A branch instruction replaces the contents of PC with the branch target address, which is usually obtained by adding an offset X given in the branch instruction.
The offset X is usually the difference between the branch target address and the address immediately following the branch instruction.
Example Branch instruction in 2000
Branch target in 2050.
Value of X must be 46

## Slide 18
Step
Action
1
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
2
Z
out
,
PC
in
,
Y
in
,
WMF
C
3
MDR
out
,
IR
in
4
Offset-field-of-IR
out
,Select y,
Add,
Z
in
5
Z
out
,
PC
in
,
End
Figure 7.7. Control sequence for an unconditional branch instruction.

## Slide 19
Some Fundamental Concepts
Execution of a Complete Instruction
Hardwired Control
Microprogrammed Control

## Slide 20: Overview
To execute instructions, the processor must have some means of generating the control signals needed in the proper sequence.
Two categories: hardwired control and microprogrammed control
Hardwired system can operate at high speed; but with little flexibility.

## Slide 21: Control Unit Organization
Figure 7.10. Control unit organization.
CLK
Clock
Control step
IR
encoder
Decoder/
Control signals
codes
counter
inputs
Condition
External

## Slide 22: Decoding and Encoding Functions

## Slide 23: Generating Zin
Zin = T1 + T6 • ADD + T4 • BR + …
Figure 7.12. Generation of the Zin control signal for the processor in Figure 7.1.
T
1
Add
Branch
T
4
T
6

## Slide 24: Generating End
End = T7 • ADD + T5 • BR + (T5 • N + T4 • N) • BRN +…

## Slide 25: A Complete Processor

## Slide 26
Some Fundamental Concepts
Execution of a Complete Instruction
Hardwired Control
Microprogrammed Control

## Slide 28
Control signals are generated by a program similar to machine language programs.
Control Word (CW) – word whose individual bit represents the various control signals
Microroutine- Sequence of control words corresponding to the control sequence of a machine instruction
Microinstruction – individual control words in this microroutine
Control store – Microroutine for all in the instruction set are stored in special memory called control store
Micro Program Counter(µPC) - to read a control word sequentially from the control store
Every time a new instruction is loaded into the IR, output of the block “starting address generator” is loaded into the µPC
µPC is automatically incremented by the clock, causing successive microinstructions to be read from the control store

## Slide 30
The previous organization cannot handle the situation when the control unit is required to check the status of the condition codes or external inputs to choose between alternative courses of action.
Use conditional branch microinstruction.
Address
Microinstruction
0
PC
out
,
MAR
in
,
Read,
Select4,
Add,
Z
in
1
Z
out
,
PC
in
,
Y
in
,
WMF
C
2
MDR
out
,
IR
in
3
Branch
to
starting
address
of
appropriate
microroutine
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
25
If
N=0,
then
branch
to
microinstruction
0
26
Offset-field-of-IR
out
,
SelectY,
Add,
Z
in
27
Z
out
,
PC
in
,
End
Figure 7.17. Microroutine for the instruction Branch<0.

## Slide 31
Figure 7.18. Organization of the control unit to allow
conditional branching in the microprogram.
Control
store
Clock
generator
Starting and
branch address
Condition
codes
inputs
External
CW
IR
m
P
C

## Slide 32: Microinstructions
A straightforward way to structure microinstructions is to assign one bit position to each control signal.
However, this is very inefficient.
The length can be reduced: most signals are not needed simultaneously, and many signals are mutually exclusive.
All mutually exclusive signals are placed in the same group in binary coding.
At most one microoperation per group is specified in one microinstruction.

## Slide 34: Microprogram Sequencing
If all microprograms require only straightforward sequential execution of microinstructions except for branches, letting a μPC governs the sequencing would be efficient.
However, two disadvantages:
  Having a separate microroutine for each machine instruction results in a large total number of microinstructions and a large control store.
  Longer execution time because it takes more time to carry out the required branches.
Example: Add src, Rdst
Four addressing modes: register, autoincrement, autodecrement, and indexed (with indirect forms).

## Slide 35
- Bit-ORing
- Wide-Branch Addressing
- WMFC

## Slide 36
Branch Address Modification using Bit-ORing
  At point labeled ∞, it is necessary to choose between actions required by direct and indirect addressing modes
  Indirect mode – 171
  Direct mode – 170
  Branch micro instruction and specify the address 170 and use an OR gate to change the least significant bit of this address to 1 if the direct addressing mode is involved, known as bit-ORing technique

## Slide 37
Thank You