## Slide 1: The Memory System

## Slide 2
The Main Memory, Memory Hierarchy
RAM
ROM
Cache Memory
Performance Considerations
Virtual Memory

## Slide 3: Some Basic Concepts
No. of locations in memory represents the size of address space. Eg 16 bit – 64K, 32 bit-4G
Byte-addressable
  Fig…
  In a 32 bit address – higher order 30 bits determine which word could be accessed
  If a byte quantity is specified, the lower order 2 bits specify which byte location is involved

## Slide 4
Up to 2
k
addressable
MDR
MAR
k
-bit
address bus
n
-bit
data bus
Control lines
( , MFC, etc.)
Processor
Memory
locations
Word length =
n
bits
W
R
/

## Slide 5
Data transfer between memory and processor
  Two processor registers – MAR & MDR
  MAR – k bits long, memory has 2k addressable locations, k lines for address bus
  MDR – n bits long, n bits of data are transferred between memory and processor, data bus has n lines
  Bus includes control lines Read/Write/(R/W) and MFC (Memory Function Completed)

## Slide 6
Memory Read
  Address in MAR
  Set R/W to 1
  Memory place the data from memory location to data lines and signal through MFC
  Processor loads data on data lines to MDR
Memory Write
  Load the address into MAR and data into MDR
  Set R/W to 0

## Slide 7
Measures for the speed of a memory:
  Memory access time – time between Read and MFC signals
  Memory cycle time – minimum time delay between the initiation of two successive memory operations
RAM and Secondary Storage(Serial)
An important design issue is to provide a computer system with as large and fast a memory as possible, within a given cost target.
Techniques to increase the effective size and speed of the memory:
  Cache memory (to increase the effective speed).
  Virtual memory (to increase the effective size).

## Slide 8: Memory Hierarchy
Pr
ocessor
Primary
cache
Main
memory
Increasing
size
Increasing
speed
Magnetic disk
secondary
memory
Increasing
cost per bit
Re
gisters
L1
Secondary
cache
L2
Fastest access is to the data held in
processor registers. Registers are at
the top of the memory hierarchy.
Relatively small amount of memory that
can be implemented on the processor
chip. This is processor cache.
Two levels of cache. Level 1 (L1) cache
is on the processor chip. Level 2 (L2)
cache is in between main memory and
processor.
Next level is main memory. Much larger,
but much slower than cache memory.
Next level is magnetic disks. Huge amount
of inexepensive storage.
Speed of memory access is critical, the
idea is to bring instructions and data
that will be used in the near future as
close to the processor as possible.

## Slide 9
The Main Memory, Memory Hierarchy
RAM
ROM
Cache Memory
Performance Considerations
Virtual Memory

## Slide 10: Internal organization of memory chips
Each memory cell can hold one bit of information.
Memory cells are organized in the form of an array.
One row is one memory word.
All cells of a row are connected to a common line, known as the “word line”.
Word line is connected to the address decoder.
Sense/write circuits are connected to the data input/output lines of the memory chip.
2 control lines – R/W , CS
Fig…
16x8 organization ie 16words of 8 bit each

## Slide 11
FF
circuit
Sense / Write
Address
decoder
FF
CS
cells
Memory
circuit
Sense / Write
Sense / Write
circuit
Data input
/output lines:
A
0
A
1
A
2
A
3
W
0
W
1
W
15
7
1
0
W
R
/
7
1
0
b
7
b
1
b
0
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•
•

## Slide 12: Static memories
“Memories that consists of circuits capable of retaining
their state as long as power is applied ” – static memories
Fig… Static RAM(SRAM)
Two transistor inverters are cross connected to implement a basic flip-flop.
The cell is connected to one word line and two bits lines by transistors T1 and T2
When word line is at ground level, the transistors are turned off and the latch retains its state
Eg. If the cell is in state 1, X is 1 and Y is 0

## Slide 13
Y
X
Word line
Bit lines
b
T
2
T
1
b
¢

## Slide 14
Read operation
  Word line is activated to close switches T1 and T2
  Sense/Write circuits at the bottom monitor the state of b and b’
Write Operation
  The state of the cell is set by placing the appropriate value on bit line b and its complement on b’ and the activate word line

## Slide 15
Static RAMs (SRAMs):
  Consist of circuits that are capable of retaining their state as long as the power is applied.
  Volatile memories, because their contents are lost when power is interrupted.
  Access times of static RAMs are in the range of few nanoseconds.
  However, the cost is usually high.
Dynamic RAMs (DRAMs):
  Do not retain their state indefinitely.
  Contents must be periodically refreshed.
  Contents may be refreshed while accessing them for reading.

## Slide 16: Asynchronous DRAMs
Dynamic memory cell – Information is stored in the form of a charge on a capacitor
Charge can be maintained for only tens of milliseconds
Contents are periodically refreshed by restoring the capacitor charge to its full value
Fig… Memory cell consists of capacitor, C and transistor, T
To store, transistor T is turned on, and voltage is applied to the bit line
After the transistor is turned off, the capacitor begins to discharge.
During Read, the transistor is turned on
A sense amplifier detects the charge. If it is above threshold, it drives the bit line to full charge(1). If it is below threshold, it pulls the bit line to ground level(0)
Reading will automatically refreshes its contents
T
C

## Slide 17
Column
CS
Sense / Write
circuits
cell array
latch
address
Row
Column
latch
decoder
Row
decoder
address
4096
512
8
´
(
)
´
R
/
W
A
20
9
-
A
8
0
-
¤
D
0
D
7
R
A
S
C
A
S

## Slide 18
16Mega bit DRAM chip which is organized as 4kx4k array
Each row can store 512 bytes(512x8). 12 bits to select a row, and 9 bits to select a group in a row. Total of 21 bits.
First apply the row address, RAS(Row Address Strobe) signal latches the row address.
Then apply the column address, CAS(Column Address Strobe) signal latches the address.
Read – the output values of the selected circuits are transferred to D7-0
Write – Information on D7-0 are transferred to the selected circuits
A refresh circuit will do refreshing
Timing of the memory unit is controlled asynchronously and hence it is asynchronous DRAM

## Slide 19: Fast Page Mode
Suppose if we want to access the consecutive bytes in the selected row.
This can be done without having to reselect the row.
  Add a latch at the output of the sense circuits in each column.
  All the latches are loaded when the row is selected.
  Different column addresses can be applied to select and place different bytes on the data lines.
Consecutive sequence of column addresses can be applied under the control signal CAS, without reselecting the row.
  Allows a block of data to be transferred at a much faster rate than random accesses.
  A small collection/group of bytes is usually referred to as a block.
This transfer capability is referred to as the
fast page mode feature.

## Slide 20: Synchronous DRAMs
R
/
W
R
A
S
C
A
S
C
S
Clock
Cell array
latch
address
Row
decoder
Ro
w
decoder
Co
lumn
Read/Write
circuits & latches
counter
address
Column
Row/Column
address
Data input
register
Data output
register
Data
Refresh
counter
Mode register
and
timing control

## Slide 21
Operation is directly synchronized with processor clock signal.
The outputs of the sense circuits are connected to a latch.
During a Read operation, the contents of the cells in a row are
loaded onto the latches.
During a refresh operation, the contents of the cells are refreshed without changing the contents of the latches.
Data held in the latches correspond to the selected columns are transferred to the output.
SDRAMs have different modes of operations which can be selected by writing control information into a mode register

## Slide 22: Latency, Bandwidth and DDRSDRAMs
Memory latency is the time it takes to transfer a word of data to or from memory
Memory bandwidth is the number of bits or bytes that can be transferred in one second.
DDRSDRAMs(Double-data-rate SDRAMs)
  Data transfer happens on both edges of clock
  Cell array is organized in two banks
  Each bank can be accessed separately
  Consecutive word of a given block are stored in different banks

## Slide 23
The Main Memory, Memory Hierarchy
RAM
ROM
Cache Memory
Performance Considerations
Virtual Memory
Secondary Storage

## Slide 24: Read-Only Memories (ROMs)
SRAM and SDRAM chips are volatile:
  Lose the contents when the power is turned off.
Many applications need memory devices to retain contents after the power is turned off.
  For example, computer is turned on, the operating system must be loaded from the disk into the memory.
  Store instructions which would load the OS from the disk.
  Need to store these instructions so that they will not be lost after the power is turned off.
  We need to store the instructions into a non-volatile memory.
Non-volatile memory is read in the same manner as volatile memory.
  Separate writing process is needed to place information in this memory.
  Normal operation involves only reading of data, this type
  of memory is called Read-Only memory (ROM).

## Slide 25: Read-Only Memories (Contd.,)
Read-Only Memory:
  Data are written into a ROM when it is manufactured.
  Logical 0 is stored in the cell when T is connected to the ground at point P else a logical 1 is stored.
  TO READ:
    The Word line is activated, T closes voltage sensed at bit line
    IF 0 is stored then T is grounded and voltage will low.
    If 1 is stored then no connection to ground and High voltage is sensed.
    The sense circuit at the end of bit line generates proper output value

## Slide 26
Programmable Read-Only Memory (PROM):
  Allow the data to be loaded by a user.
  Insert fuse at point P
  Before it is programmed, memory contains all 0s
  User can insert 1s at the required locations by burning out the fuses at these locations using high current pulses
  Process of inserting the data is irreversible.
  Storing information specific to a user in a ROM is expensive.
Erasable Programmable Read-Only Memory (EPROM):
  Stored data to be erased and new data to be loaded.
  Erasable, reprogrammable ROM.
  Erasure requires exposing the ROM to UV light.

## Slide 27
Electrically Erasable Programmable Read-Only Memory (EEPROM):
  Disadvantage of EPROM is that chip must be physically removed from the circuit for programming
  EEPROM is both programmed and erased electrically
  Do not have to be removed for erasure
  Possible to erase the cell contents selectively
  Disadvantage is that different voltages are needed for erasing, writing and reading the stored data