## Slide 1: Cache Memory

## Slide 2
The Main Memory, Memory Hierarchy
RAM
ROM
Cache Memory
Secondary Memory
Performance Considerations
Virtual Memory

## Slide 3: Cache Memories
Processor is much faster than the main memory.
  As a result, the processor has to spend much of its time waiting while instructions and data are being fetched from the main memory.
  Major obstacle towards achieving good performance.
Speed of the main memory cannot be increased beyond a certain point.
Cache memory is an architectural arrangement which makes the main memory appear faster to the processor than it really is.
Cache memory is based on the property of computer programs known as “locality of reference”.

## Slide 4: Locality of Reference
Many instructions in localized areas of a program are executed repeatedly during some period of time, while the others are accessed relatively less frequently.
  These instructions may be the ones in a loop, nested loop or few procedures calling each other repeatedly.
  This is called “locality of reference”.
Temporal locality of reference:
  Recently executed instruction is likely to be executed again very soon.
Spatial locality of reference:
  Instructions with addresses close to a recently instruction are likely to be executed soon.

## Slide 5: Cache memories
Processor issues a Read request, a block of words is transferred from the main memory to the cache, one word at a time.
At any given time, only some blocks in the main memory are held in the cache. Which blocks in the main memory are in the cache is determined by a “mapping function”.
When the cache is full, and a block of words needs to be transferred from the main memory, some block of words in the cache must be replaced. This is determined by a “replacement algorithm”.
Cache
Main
memory
Processor

## Slide 6: Cache hit
Existence of a cache is transparent to the processor. The processor issues Read and Write requests in the same manner.
If the data is in the cache it is called a Read or Write hit.
Read hit:
  The data is obtained from the cache.
Write hit:
  Cache has a replica of the contents of the main memory.
  Contents of the cache and the main memory may be updated simultaneously. This is the write-through protocol.
  Update the contents of the cache, and mark it as updated by setting a bit known as the dirty bit or modified bit. The contents of the main memory are updated when this block is replaced. This is write-back or copy-back protocol.

## Slide 7: Cache miss
If the data is not present in the cache, then a Read miss or Write miss occurs.
Read miss:
  Block of words containing this requested word is transferred from the memory.
  After the block is transferred, the desired word is forwarded to the processor.
  The desired word may also be forwarded to the processor as soon as it is transferred without waiting for the entire block to be transferred. This is called load-through or early-restart.
Write-miss:
  Write-through protocol is used, then the contents of the main memory are updated directly.
  If write-back protocol is used, the block containing the addressed word is first brought into the cache. The desired word
  is overwritten with new information.

## Slide 8: Mapping functions
Mapping functions determine how memory blocks are placed in the cache.
A simple processor example:
  Cache consisting of 128 blocks of 16 words each.
  Total size of cache is 2048 (2K) words.
  Main memory is addressable by a 16-bit address.
  Main memory has 64K words.
  Main memory has 4K blocks of 16 words each.
Three mapping functions:
  Direct mapping
  Associative mapping
  Set-associative mapping.

## Slide 9: Direct mapping
Main
memory
Block 0
Block 1
Block 127
Block 128
Block 129
Block 255
Block 256
Block 257
Block 4095
7
4
Main memory address
T
ag
Block
W
ord
5
tag
tag
tag
Cache
Block 0
Block 1
Block 127
Block j of the main memory maps to j modulo 128 of the cache. 0 maps to 0, 129 maps to 1.
More than one memory block is mapped onto the same
position in the cache.
May lead to contention for cache blocks even if the cache is not full.
Resolve the contention by allowing new block to replace the old block, leading to a trivial replacement algorithm.
Memory address is divided into three fields:
- Low order 4 bits determine one of the 16 words in a block.
- When a new block is brought into the cache, the next 7 bits determine which cache block this new block is placed in.
- High order 5 bits determine which of the possible 32 blocks is currently present in the cache. These are tag bits.
Simple to implement but not very flexible.

## Slide 10: Associative mapping
Main memory block can be placed into any cache
position.
Memory address is divided into two fields:
- Low order 4 bits identify the word within a block.
- High order 12 bits or tag bits identify a memory
block when it is resident in the cache.
Flexible, and uses cache space efficiently.
Replacement algorithms can be used to replace an
existing block in the cache when the cache is full.
Cost is higher than direct-mapped cache because of
the need to search all 128 patterns to determine
whether a given block is in the cache.
Main
memory
Block 0
Block 1
Block 127
Block 128
Block 129
Block 255
Block 256
Block 257
Block 4095
4
Main memory address
Tag
Word
12
tag
tag
tag
Cache
Block 0
Block 1
Block 127

## Slide 11: Set-Associative mapping
Blocks of cache are grouped into sets.
Mapping function allows a block of the main
memory to reside in any block of a specific set.
Divide the cache into 64 sets, with two blocks per set.
Memory block 0, 64, 128 etc. map to block 0, and they can occupy either of the two positions.
Memory address is divided into three fields:
- 6 bit field determines the set number.
- High order 6 bit fields are compared to the tag
fields of the two blocks in a set.
Set-associative mapping combination of direct and associative mapping.
Main
memory
Block 0
Block 1
Block 63
Block 64
Block 65
Block 127
Block 128
Block 129
Block 4095
6
4
Main memory address
T
ag
set
W
ord
6
tag
tag
tag
Cache
Block 1
Block 2
Block 126
Block 127
Block 3
Block 0
tag
tag
tag

## Slide 12: Replacement algorithms
LRU
  When a block is to be overwritten, overwrite the one that has gone the longest time without being referenced – called least recently used(LRU) block
  The technique is called LRU replacement algorithm
  To track the LRU block of a four block set, a 2 bit counter can be used for each block
  When a hit occurs the counter of the block referenced is set to 0
  Counter with values lower than the referenced are incremented by 1 and others are unchanged
  When a miss occurs and the set is not full, new block is loaded from memory and set counter to 0.
  When a miss occurs and the set is full, block with counter value 3 is removed, new block is put and set counter to 0.

## Slide 13
The Main Memory, Memory Hierarchy
RAM
ROM
Cache Memory
Performance Considerations
Virtual Memory
Memory Management Requirements

## Slide 14: Performance considerations
A key design objective of a computer system is to achieve the best possible performance at the lowest possible cost.
  Price/performance ratio is a common measure of success.
Performance of a processor depends on:
  How fast machine instructions can be brought into the processor for execution.
  How fast the instructions can be executed.
Memory hierarchy plays an important role in Price/ performance ratio.
The speed and efficiency of data transfer at different levels in the hierarchy are very important.
The best: If the transfer to and from a faster unit can be done at a rate equal to the faster unit.
This is not possible if transfer is between fast and slow unit.

## Slide 15
An effective way is to use an interleaved organization (parallelism).

## Slide 16: Interleaving
Divides the memory system into a number of memory modules.
  Each module has its own address buffer register (ABR) and data buffer register (DBR).
Arranges addressing so that successive words in the address space are placed in different modules.
When requests for memory access involve consecutive addresses, the access will be to different modules.
Since parallel access to these modules is possible, the average rate of fetching words from the Main Memory can be increased.

## Slide 17: Consecutive words in module
Consecutive words are placed in a module.
High-order k bits of a memory address determine the module.
Low-order m bits of a memory address determine the word within a module.
When a block of words is transferred from main memory to cache, only one module is busy at a time.
m
bits
Address in module
MM address
i
k
bits
Module
Module
Module
Module
DBR
ABR
DBR
ABR
ABR
DBR
0
n
1
-

## Slide 18: Consecutive words in consecutive modules
i
k
bits
0
Module
Module
Module
Module
MM address
DBR
ABR
ABR
DBR
ABR
DBR
Address in module
2
k
1
-
m
bits
Consecutive words are located in consecutive modules.
Consecutive addresses can be located in consecutive modules.
While transferring a block of data, several memory modules can be kept busy at the same time.

## Slide 19: Hit rate and Miss Penalty
Effectiveness of a particular memory hierarchy is indicated by the success rate in accessing information at various levels.
A HIT occurs when access of data is successful.
No: of hits to no: of all attempted accesses is called HIT rate.
No: of misses to no: of all attempted accesses is called MISS rate.
High HIT rates > 0.9 are required for high performance computers.

## Slide 20: MISS Penalty
Performance is affected by the actions taken after a MISS occurs.
The extra time needed to bring the desired information into the cache is called MISS penalty.
MISS Penalty is the time required to get a block from a slow memory unit to a faster unit.
This is reduced with efficient mechanism in data transferring : Interleaved memory