## Slide 1: Flynn's Classical Taxonomy

## Slide 2: Flynn's Classical Taxonomy (William Stallings)
There are different ways to classify parallel computers. One of the more widely used classifications, in use since 1966, is called Flynn's Taxonomy.
Flynn's taxonomy distinguishes multi-processor computer architectures according to how they can be classified along the two independent dimensions of Instruction and Data.
Each of these dimensions can have only one of two possible states: Single or Multiple.

## Slide 3: Flynn's Classical Taxonomy
    Single Instruction Stream , Single Data Stream(SISD)
    Single Instruction Stream , Multiple Data Stream(SIMD)
    Multiple Instruction Stream , Multiple Data Stream(MIMD)
    Multiple Instruction Stream , Single Data Stream(MISD)

## Slide 4: 1.Single Instruction Stream Single Data Stream(SISD)
CU
PU
MM
IS
IS
DS
SISD Computer

## Slide 5: SISD
Single Instruction: Only one instruction stream is being acted on by the CPU during any one clock cycle
Single Data: Only one data stream is being used as input during any one clock cycle
Single processor
Single instruction stream
Data stored in single memory
Uni-processor

## Slide 6: 2. Single Instruction Stream Multiple Data Stream(SIMD)
This class corresponds to array processors
There are multiple processing elements supervised by the same control unit
All Processing unit receive the same instruction broadcast from the control unit but operate on different data sets from distinct data streams

## Slide 7: SIMD
Single Instruction: All processing units execute the same instruction at any given clock cycle
Multiple Data: Each processing unit can operate on a different data element

## Slide 8: SIMD
Single machine instruction
Controls simultaneous execution
Number of processing elements
Each processing element has associated data memory
Each instruction executed on different set of data by different processors
Vector and array processors

## Slide 9: 2.1 VECTOR PROCESSING (Morris Mano)
There is a class of computational problems that are beyond the capabilities of a conventional computer. These problems require a vast number of computations that will take a conventional computer days or even weeks to complete.
Vector Processing Applications
Problems that can be efficiently formulated in terms of vectors and matrices
  Long-range weather forecasting - Petroleum explorations
  Seismic data analysis - Medical diagnosis
  Aerodynamics and space flight simulations
  Artificial intelligence and expert systems
  Mapping the human genome
  Image processing
Vector Processor (computer)
Ability to process vectors, and matrices much faster than conventional computers

## Slide 10: VECTOR PROGRAMMING
DO 20 I = 1, 100
20 C(I) = B(I) + A(I)
Conventional computer (Mahine language)
Initialize I = 0
20 Read A(I)
Read B(I)
Store C(I) = A(I) + B(I)
Increment I = I + 1
If I  100 goto 20
Vector computer
C(1:100) = A(1:100) + B(1:100)
Fortran Language

## Slide 11
  Vector Instruction Format :
  ADD A B C 100
  Matrix Multiplication
    3 x 3 matrices multiplication :

## Slide 12
  Pipeline for calculating an inner product :
    Floating point multiplier pipeline : 4 segments
    Floating point adder pipeline : 4 segments
      after 1st clock input
      after 4th clock input
A1B1
A4B4 A3B3 A2B2 A1B1
0
0
0
0
0
0
0
0
0
0
0

## Slide 13
      after 8th clock input
      after 9th, 10th, 11th ,...
A8B8 A7B7 A6B6 A5B5 A4B4 A3B3 A2B2 A1B1
A9B9 A8B8 A7B7 A6B6 A4B4 A3B3 A2B2
A1B1
+
A5B5

## Slide 14: MEMORY INTERLEAVING
Pipeline and vector processors often require simultaneous access to memory from two or more sources.
An instruction pipeline may require the fetching of an instruction and an operand at the same time from two different segments.
An arithmetic pipeline usually requires two or more operands to enter the pipeline at the same time.
Instead of using two memory buses for simultaneous access, the memory can be partitioned into a number of modules connected to common memory address and data buses.
Address Interleaving
Different sets of addresses are assigned to different memory modules
For example, in a two-module memory system, the even addresses may be in one module and the odd addresses in the other.

## Slide 15
Vector Processing
A vector processor that uses an n-way interleaved memory can fetch n operands from n different modules. By staggering the memory access, the effective memory cycle time can be reduced by a factor close to the number of modules.
A CPU with instruction pipeline can take advantage of multiple memory modules so that each segment in the pipeline can access memory independent of memory access from other segments.
AR
Memory
array
DR
AR
Memory
array
DR
AR
Memory
array
DR
AR
Memory
array
DR
Address bus
Data bus
M0 M1 M2 M3

## Slide 16
  Performs computations on large arrays of data
    Attached array processor :
      Auxiliary processor attached to a general purpose computer to improve the numerical computation performance.
    SIMD array processor :
      Computer with multiple processing units operating in parallel
        Vector C = A + B ci = ai + bi
  Although both types manipulate vectors, their internal organization is different.
2.2 Array Processors

## Slide 17
Attached array processor
Designed as a peripheral for complex scientific applications attached with a conventional host computer.
The peripheral is treated like an external interface. The data are transferred from main memory to local memory through high-speed bus.
The general-purpose computer without the attached processor serves the users that need conventional data processing.

## Slide 18
Vector instructions are broadcast to all PEs simultaneously
Example: C = A + B
  The master control unit first stores the i th components ai and bi in local
  memory Mi for i = 1, 2, …, n.
  Broadcasts the floating-point add instruction ci = ai + bi to all PEs
  The components of ci are stored in fixed locations in each local
  memory.
SIMD array processor
Scalar and program control instructions are directly executed within the master control unit.

## Slide 19: 3. Multiple Instruction Stream Single Data Stream(MISD) (William Stallings)
There are n processor units each receiving distinct instructions operating over the same data stream and its derivatives
The result of one processor becomes the input of the next processor .
CU1
CU2
CUn
IS1
PU1
PU2
PUn
IS2
ISn
IS1
IS2
ISn
MM1
MM2
MMn
DS
IS1
IS2
ISn
DS

## Slide 20: MISD
Multiple Instruction: Each processing unit operates on the data independently via separate instruction streams.
Single Data: A single data stream is fed into multiple processing units.

## Slide 21: MISD
Sequence of data
Transmitted to set of processors
Each processor executes different instruction sequence
Never been implemented

## Slide 22: 4.Multiple Instruction Stream Multiple Data Stream(MIMD)
All memory streams are derived from the same data space shared by all processors
It is a set of n independent SISD uniprocessor systems
CU1
CU2
CUn
PU1
PU2
PUn
IS1
IS2
ISn
MM1
MM2
MMn
IS1
IS2
ISn
DS1
DS2
DSn

## Slide 23: MIMD
Multiple Instruction: Every processor may be executing a different instruction stream.
Multiple Data: Every processor may be working with a different data stream.