## Slide 1: Pipelining
1.Basic Concepts

## Slide 2: Traditional Pipeline Concept
Laundry Example
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, and fold
Washer takes 30 minutes
Dryer takes 40 minutes
“Folder” takes 20 minutes
A
B
C
D

## Slide 3: Traditional Pipeline Concept
Sequential laundry takes 6 hours for 4 loads
If they learned pipelining, how long would laundry take?
A
B
C
D
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 4: Traditional Pipeline Concept
Pipelined laundry takes 3.5 hours for 4 loads
A
B
C
D
6 PM
7
8
9
10
11
Midnight
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 5: Traditional Pipeline Concept
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20

## Slide 6: Pipelining in a Computer
F
1
E
1
F
2
E
2
F
3
E
3
I
1
I
2
I
3
(a) Sequential execution
Instruction
fetch
unit
Ex
ecution
unit
Interstage buffer
B1
(b) Hardware organization
T
ime
F
1
E
1
F
2
E
2
F
3
E
3
I
1
I
2
I
3
Instruction
(c) Pipelined execution
Figure 8.1. Basic idea of instruction pipelining.
Clock cycle
1
2
3
4
T
ime
Fetch + Execution

## Slide 7: Use the Idea of Pipelining in a Computer
Fetch + Decode
+ Execution + Write

## Slide 8: Pipelining in Computer
    Decomposing a sequential process into sub operations
    Each sub process is executed in a special dedicated segment concurrently
  Pipelining:
    Multiply and add operation : ( for i = 1, 2, …, 7 )
    3 Suboperation Segment
      1) : Input Ai and Bi
      2) : Multiply and input Ci
      3) : Add Ci

## Slide 9: 1.Role of Cache Memory
Each pipeline stage is expected to complete in one clock cycle.
The clock period should be long enough to let the slowest pipeline stage to complete.
Faster stages can only wait for the slowest one to complete.
Since main memory is very slow compared to the execution, if each instruction needs to be fetched from main memory, pipeline is almost useless.
Fortunately, we have cache.

## Slide 10: 2.Pipeline Performance
The potential increase in performance resulting from pipelining is proportional to the number of pipeline stages.
However, this increase would be achieved only if all pipeline stages require the same time to complete, and there is no interruption throughout program execution.
Unfortunately, this is not true.

## Slide 11: Pipeline Performance

## Slide 12: Pipeline Performance
The previous pipeline is said to have been stalled for two clock cycles.
Any condition that causes a pipeline to stall is called a hazard.
Data hazard – any condition in which either the source or the destination operands of an instruction are not available at the time expected in the pipeline. So some operation has to be delayed, and the pipeline stalls.
Instruction (control) hazard – a delay in the availability of an instruction causes the pipeline to stall.
Structural hazard – the situation when two instructions require the use of a given hardware resource at the same time.

## Slide 13: Pipeline Performance
Idle periods – stalls (bubbles)
Instruction hazard
Eg. Cache miss

## Slide 14: Pipeline Performance
Load X(R1), R2
Structural hazard
- Access to memory

## Slide 15: Pipeline Performance
Again, pipelining does not result in individual instructions being executed faster; rather, it is the throughput that increases.
Throughput is measured by the rate at which instruction execution is completed.
Pipeline stall causes degradation in pipeline performance.
We need to identify all hazards that may cause the pipeline to stall and to find ways to minimize their impact.