## Slide 1: 2.Data Hazards

## Slide 2: Data Hazards
We must ensure that the results obtained when instructions are executed in a pipelined processor are identical to those obtained when the same instructions are executed sequentially.
Hazard occurs
Let A=5
A ← 3 + A
B ← 4 × A
No hazard
A ← 5 × C
B ← 20 + C
Data dependency arises when the destination of one instruction is used as the source in the next instruction.
Another example:
Mul R2, R3, R4
Add R5, R4, R6

## Slide 3: Data Hazards
Figure 8.6. Pipeline stalled by data dependency between D2 and W1.
Mul R2, R3, R4
Add R5, R4, R6

## Slide 4: Operand Forwarding
Instead of from the register file, the second instruction can get data directly from the output of ALU after the previous instruction is completed.
A special arrangement needs to be made to “forward” the output of ALU to the input of ALU.

## Slide 5
I1:Mul R2, R3, R4
I2:Add R5, R4, R6
Decoding I2,
detecting data dependency, decide to use data forwarding
The operand not dependent, R5 is loaded to SRC1 in clock cycle3
In the next clock cycle, the product available in RSLT can be forwarded and used in I2

## Slide 6: Handling Data Hazards in Software
Let the compiler detect and handle the hazard:
I1: Mul R2, R3, R4
NOP
NOP
I2: Add R5, R4, R6
The compiler can reorder the instructions to perform some useful work during the NOP slots.