## Slide 1: Multiprocessors

## Slide 2: The Structure of general purpose multiprocessors

## Slide 3: UMA
Permits n processors to access k memories
Interconnection network may introduce a delay
If delay is same for all accesses to memory, such a machine is called uniform memory access
.

## Slide 4: NUMA

## Slide 5: NUMA
Attach a memory module directly to the processor
Processor can also access other memories, which will be longer than access to the local memory
Such a machine is called Non uniform memory access
.

## Slide 6: Distributed Memory System

## Slide 7: Distributed Memory System
All memory module serve as private memory for the processor
A processor access a remote memory by exchanging messages to the processor
Such a system is called distributed-memory systems with a message-passing protocol
.

## Slide 8: Interconnection Networks
Suitability of a network
  Cost
  Bandwidth – Capacity of a transmission link to transfer data (bits or bytes per second)
  Throughput – Rate if data transfer
  Ease of implementation

## Slide 9: Single Bus
Bus transfer take T time units, memory access time is 4T units
Split-Transaction protocol – use the bus in the idle period to serve another request
Disadv – the number of modules connected to the bus is not large

## Slide 10: Crossbar Networks

## Slide 11: Crossbar Networks
Fully connected network – Any module can be connected to any other module by closing an appropriate switch
Also called non-blocking switch

## Slide 12: Multistage Networks

## Slide 13: Multistage Networks
Less costly
Large number of parallel paths between sources and destinations

## Slide 14: Hypercube Networks

## Slide 15: Hypercube Networks
N-dimensional cube that interconnects 2n nodes
Each node is directly connected to n neighbors
Label nodes by binary address
Send message to all neighbors
Maximum distance that the message need to travel is n hops

## Slide 16: Mesh Networks

## Slide 17: Mesh Networks
Link between the nodes are bidirectional
For routing, first the transfer takes place in horizontal direction and then in vertical direction

## Slide 18: Tree Networks

## Slide 19: Tree Networks
4 way tree that interconnects 16 modules
  Each parent node allows communication between 2 of its children at a time
Fat tree network
  Number of links in the upper levels of the tree hierarchy

## Slide 20: Ring Networks

## Slide 21: Ring Networks
Easy to implement
Short rings reduces the latency of transfer
Hierarchy of rings

## Slide 22: Memory Organization

## Slide 23: Memory Organization
Processor include primary cache and secondary cache
Single global address space where a range of physical address is assigned to each memory module

## Slide 24: Memory Organization

## Slide 25: Memory Organization
NUMA – each node contain a processor and portion of the memory
Each memory module constitutes the private address space of that processor